## Slide 1: 2015 FRC Control System
101010 = MOL = DUK

## Slide 2: 2014 Power Distribution Board
+ 12 Volts
-12 Volts
(4)
40 amp Circuits
40 amp Circuits
(4)
(6)
20/30 amp Circuits
20/30 amp Circuits
(6)
12 Volt
(DAP Bridge)
5 Volt
(Camera)
24 Volt
(cRIO)

## Slide 3: 2015 Power Distribution Panel
(4)
40 amp Circuits
40 amp Circuits
(4)
(4)
20/30 amp Circuits
20/30 amp Circuits
(4)
+ 12 Volts
-12 Volts
CAN
RoboRIO
PCM
VRM
Voltage Regulator Module
Pneumatic Control Module

## Slide 4: 2014 NI 4-Slot cRIO
24v DC Power
Serial Port
Ethernet Port
Analog Module
Digital Module
Solenoid Module
(Optional)
Optional:
Analog Module
Digital Module
Solenoid Module

## Slide 5: Digital Side Car – Analog Breakout
37-pin Connector
(cRIO Digital Module)
PWM Outputs (10)
(Motor Controllers and Servos)
12v Power
Input
Digital Input/Output (14)
Relay Output (8)
Relay Status
LEDs
I2C Header and Connector
Robot Signal
Light
12v Power
Input
Analog Inputs (8)
Connector (DB25)
(cRIO Analog Module)
12-bit ADC with range of -10 to +10 Vdc
(With 0 -5 Vdc input ADC counts = 0 to 1023)
Battery Voltage
Jumper

## Slide 6: 2015 NI RoboRIO
CAN = Controller Area Network
DIO = Digital Input / Output
I2C = Inter-Integrated Circuit
MXP = myRIO Expansion Port
PWM = Pulse Width Modulation
RS232 = Serial Port Standard
RSL = Robot Signal Light
SPI = Serial Peripheral Interface
12v Power
USB Device
Ethernet
SPI
Status LEDs
PWM (10)
CAN
I2C
RS-232
DIO (10)
Analog IN (4)
Relay (4)
RSL
USB Host
MXP
Pin Spacing = 0.1”
I/O Spacing = 0.3”
12-bit ADC with 0-5v range
Dimensions:
5.7” x 5.6” x 1.3”
Power: Green=OK
Amber=Brownout
Red=Fault
Status: On=Booting
Off=OK
Blinking=Error
Radio: NA
Comm: Off=None
Red Solid=No Code
Red Blink=E-Stop
Green Solid=OK
Mode: Off= Disabled
Green=Autonomous
Amber=Teleop
Red=Test
RSL: Off=Robot Off
On=Robot Disabled
Blinking=Robot Enabled
Accelerometer

## Slide 7: 2015 RoboRIO MXP
myRIO Expansion Port
Shared:
10 - PWM Outputs
(Disabled when Robot is Disabled)
16 - DIO
1 - I2C Port
1 - SPI Port
4 - Analog Inputs
2 - Analog Outputs
1 - RS-232 Port
http://www.usfirst.org/roboticsprograms/frc/blog-myRIO-Expansion-Port- Whats-the-Deal.

## Slide 8: 2014 Pneumatics
12/24v Power
Input
Relay Outputs (8)
(Max current/channel = 0.75A)
(Maximum Total = 21W)
Solenoid Module & Breakout
Spike Relay Digital Input

## Slide 9: 2015 Pneumatics Control Module
12v Power
CAN
Solenoid (4)
Solenoid (4)
Compressor Relay Output
Pressure Switch Input

## Slide 10: 2014 Power Converter
12v –to-5v

## Slide 11: 2015 Voltage Regulator Module
12v Power
Radio Power
Camera Power
Custom Circuits
Custom Circuits

## Slide 12: Weidmuller LSF Connectors
For best results:
Wire should be 16AWG to 24AWG (consult rules to verify required gauges for power wiring)
Wire ends should be stripped approximately 5/16“
To insert or remove the wire, press down on the corresponding "button" to open the terminal
After making the connection check to be sure that it is clean and secure:
Verify that there are no "whiskers" outside the connector that may cause a short circuit
Tug on the wire to verify that it is seated fully. If the wire comes out and is the correct gauge it
needs to be inserted further and/or stripped back further.

## Slide 13: Control System Comparison

## Slide 14: Control System Comparison

## Slide 15: RoboRIO Imaging Tool

## Slide 16: RoboRIO Networking
mDNS
Multicast Domain Name System (mDNS) is a system which allows for resolution of host names to IP addresses on small networks with no dedicated name server. (roboRIO-TEAM.local)
USB
When using the USB interface, no setup is required. The roboRIO driver will automatically configure the IP address of your computer and the roboRIO.
Wireless
The 2015 Bridge Configuration Utility will enable the DHCP (Dynamic Host Configuration Protocol) service on the DAP radio when in AP mode. The bridge is configured with a 10.TE.AM.1 IP address and will hand out DHCP addresses from 10.TE.AM.20 to 10.TE.AM.199.
When the DAP radio is in bridge mode at competitions, the FMS will be the DHCP server.
The FRC Driver Station, LabVIEW, and the Eclipse plugins for C++ and Java are all programmed to discover your roboRIO using mDNS protocol. This means the roboRIO can be detected regardless of the interface or IP being used.

## Slide 17: Bridge Configuration Utility

## Slide 18: RoboRIO Web Dashboard

## Slide 19: RoboRIO Web Dashboard

## Slide 20: RoboRIO Web Dashboard

## Slide 21: RoboRIO Web Dashboard

## Slide 22: 2015 Driver Station
ViewMenu
PC: Battery
CPU %
Battery Voltage
Chart
Log
Menu
Operation
Diagnostics
Settings
USB
CAN
Messages
Charts
Both
Messages
Operation

## Slide 23: 2015 Driver Station
Reboot
Restart
Chart
Messages + Chart
Operation
Diagnostics

## Slide 24: 2015 Driver Station
Messages
Settings
Messages
USB
6 - Joysticks
Test for Joystick Axes and Buttons

## Slide 25: DS Deleted Features
No User Messages
eStop Robotics: CCI
No Kinect
No Cypress I/O

## Slide 26: Driver Station Log Viewer

## Slide 27: Installed PDP

## Slide 28: Installed RoboRIO

## Slide 29: PDP Data Charting
Chart: Total Load
20 hz Capture Rate

## Slide 30: PDP Charting
Chart: Left Drive Motors
20 hz Capture Rate

## Slide 31: PDP Charting
Chart: 2-Ball Autonomous

## Slide 32: Feature Changes
Zero-based input/output channel numbering
Class: +Additions, -Deletions, *Changes: (C++ and Java)
+BuiltInAccelerometer -AnalogModule *AnalogAccelerometer
+PowerDistributionPanel -DigitalModule *AnalogInput
+AnalogOutput -DriverStationEnhancedIO *Compressor
-DriverStationLCD *IterativeRobot (No SetPeriod)
-Kinect
Analog-to-Digital Convertor
cRIO: -10v to +10v 12-bit 0 - 1023 (at 5v)
roboRIO: 0 to +5v 12-bit 0 - 4095
Brownout Protection
PWM outputs disabled when voltage drops below 6.50v (Restored at 7.50v)
DIO power turned off when voltage drops below 6.25v (Restored at 6.60v)
Eclipse for C++ and Java Code Development
RoboRIO mDNS: roboRIO-team.local (roboRIO-525.local)

## Slide 33: Robot Signal Light
2014 Signals
2015 Signals
STATUS | CONDITION
OFF | Robot not booted up
ON | Autonomous Enabled
ON with OFF blink every 1.5 s | Teleop Enabled
ON 900 ms, OFF 900 ms | System Disabled
ON 200 ms, OFF 900 ms | Low Battery or No User Code
ON 200 ms, OFF 200 ms | System Error
STATUS | CONDITION
OFF | Robot Off
ON | Robot Disabled
BLINKING | Robot Enabled