## Slide 1: FRC Robot Electronics

## Slide 2: NI RoboRIO
CAN = Controller Area Network
DIO = Digital Input / Output
I2C = Inter-Integrated Circuit
MXP = myRIO Expansion Port
PWM = Pulse Width Modulation
RS232 = Serial Port Standard
RSL = Robot Signal Light
SPI = Serial Peripheral Interface
12v Power
USB Device
Ethernet
SPI
Status LEDs
PWM (10)
CAN
I2C
RS-232
DIO (10)
Analog IN (4)
Relay (4)
RSL
USB Host
MXP
Pin Spacing = 0.1”
I/O Spacing = 0.3”
12-bit ADC with 0-5v range
Dimensions:
5.7” x 5.6” x 1.3”
Power: Green=OK
Amber=Brownout
Red=Fault
Status: On=Booting
Off=OK
Blinking=Error
Radio: NA
Comm: Off=None
Red Solid=No Code
Red Blink=E-Stop
Green Solid=OK
Mode: Off= Disabled
Green=Autonomous
Amber=Teleop
Red=Test
RSL: Off=Robot Off
On=Robot Disabled
Blinking=Robot Enabled
Accelerometer

## Slide 3: RoboRIO MXP
myRIO Expansion Port
Shared:
10 - PWM Outputs
(Disabled when Robot is Disabled)
16 - DIO
1 - I2C Port
1 - SPI Port
4 - Analog Inputs
2 - Analog Outputs
1 - RS-232 Port

## Slide 4: Voltage Regulator Module
12v Power
Radio Power
Camera Power
Custom Circuits
Custom Circuits

## Slide 5: Pneumatics Control Module
12v Power
CAN
Solenoid (4)
Solenoid (4)
Compressor Relay Output
Pressure Switch Input

## Slide 6: Power Distribution Panel
(4)
40 amp Circuits
40 amp Circuits
(4)
(4)
20/30 amp Circuits
20/30 amp Circuits
(4)
+ 12 Volts
-12 Volts
CAN
RoboRIO
PCM
VRM
Voltage Regulator Module
Pneumatic Control Module

## Slide 7: Motor Controllers
Jaguar
VEX Robotics
15 Khz
Talon
Cross the Road Electronics
15 Khz
Victor 888/884
VEX Robotics
1 Khz
Interface: PWM
CAN
Interface: PWM
Interface: PWM
(CAN = Controller Area Network)
WPILib Class: Jaguar
WPILib Class: Talon
WPILib Class: Victor

## Slide 8: PWM Cable
Black: Ground
Red: +5 volts
White: Signal

## Slide 9: Spike H-Bridge Relay
Control |  | OUTPUTS |  |  | 
Forward | Reverse | M+ | M- | Indicator | Motor Function
White | Red |  |  |  | 
0 | 0 | GND | GND | Orange | OFF / Brake
1 | 0 | +12v | GND | Green | Forward Rotation
0 | 1 | GND | +12v | Red | Reverse Rotation
1 | 1 | +12v | +12v | Off | OFF / Brake
WPILib Class: Relay

## Slide 10: Potentiometer
(PWM Red)
(PWM Black)
(PWM White)
Pin Color
1 Red +
2 White
3 Black -
Pin Color
1 Black -
2 White
3 Red +
Increasing
Increasing
WPILib Class: AnalogChannel

## Slide 11: Quadrature Encoder
WPILib Class: Encoder

## Slide 12: Gyro/Accelerometer
PWM Black
PWM Red
PWM White
SPI Port
(4 Digital Inputs)
I2C Port
Accelerometer
Gyro
WPILib Class: Accelerometer
WPILib Class: Gyro

## Slide 13: Photoelectric Sensors
+12/24 Vdc
-12/24 Vdc
Digital Input Signal
Photoelectric Sensors |  | 
Type | Range (Inches) | Range (mm)
Diffuse | 23.62 | 600
Diffuse with Background Suppression | 0.59 to 5.91 | 15 to 150
Polarized Reflective | 79 | 2000
Through-beam | 236 | 6000
WPILib Class: DigitalInput

## Slide 14: Limit Switches
WPILib Class: DigitalInput
Used to detect limit of travel
or stop positions.

## Slide 15: Ultrasonic Rangefinder
Ping-Response
(Digital Input and Output)
Analog
GND - PWM Black
+5 - PWM Red
AN - PWM White
WPILib Class: Ultrasonic
WPILib Class: AnalogChannel

## Slide 16: Hall Effect Sensors
WPILib Class: GearTooth

## Slide 17: PID Controller
Proportional: Present Error
Integral: Accumulation of Past Errors
Derivative: Prediction of Future Error